INTERNATIONAL ORGANISATION FOR STANDARDISATION

ORGANISATION INTERNATIONALE DE NORMALISATION

ISO/IEC JTC1/SC29/WG11

CODING OF MOVING PICTURES AND AUDIO

ISO/IEC JAhG MAR J0007

Sapporo, JP, July 2014

ISO/IEC JTC1/SC29/WG11 N14769

Sapporo, JP, July 2014

ISO/IEC JTC1/SC24/WG19 Nxxxx

August 2014

| Source | SC24 WG9 and SC29 WG11 |
| --- | --- |
| Title | Text of Mixed and Augmented Reality Reference Model Commity Draft |
| Editors | Gerard J. Kim, Christine Perey, Marius Preda |

COMMITTEE DRAFT© ISO/IEC 2014 – All rights reservedISO/IEC CD 18039 63Mixed and Augmented Reality Reference ModelInformation technology — Computer graphics, image processing and environmental data representation and Coding of audio, picture, multimedia and hypermedia informationTechnologie de l'information — Infographie, traitement d'image et données d'environment ET Codage de l'audio, image, multimédia et hypermédia — Modèle de référence pour la Réalité AugmentéeInformation technology — Computer graphics, image processing and environmental data representation and Coding of audio, picture, multimedia and hypermedia information — Mixed and Augmented Reality Reference ModelE2014-10-13(30) CommitteeISO/IECISO/IEC J   International Standard2014 ISO/IEC 18039ISO/IEC 18039ISO/IEC CD 18039  Computer graphics, image processing and environmental data representation AND Coding of audio, picture, multimedia and hypermedia informationInformation technology 24 and 291 2Titre 2,H2,H21,Œ©o‚µ 2,뙥2,?co??E 2,h2,?c1,?co?ƒÊ 2,?2,Œ1,Œ2,Œ©2,...,Œ©_o‚µ 2,Œ©1,?c_o??E 2,2,Header 2,2nd level,DO NOT USE_h2,Œ©_o...,©1,Œ??©�o‚µ 2,¨Titre 1    02 STD Version 2.1c230   4Z:\frisca\My Projects\ISO\2014.07@Sapporo\MAR RM\w14769 MAR Ref Model CD.final.doc            ISO/IEC JTC 1 Nxxxx

Date: 2014-10-13

ISO/IEC CD 18039

ISO/IEC JTC 1

Secretariat: SC24 and SC29

Information technology — Computer graphics, image processing and environmental data representation and Coding of audio, picture, multimedia and hypermedia information — Mixed and Augmented Reality Reference Model

Technologie de l'information — Infographie, traitement d'image et données d'environment ET Codage de l'audio, image, multimédia et hypermédia — Modèle de référence pour la Réalité Augmentée

Warning

This document is not an ISO International Standard. It is distributed for review and comment. It is subject to change without notice and may not be referred to as an International Standard.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

Copyright notice

This ISO document is a working draft or committee draft and is copyright-protected by ISO. While the reproduction of working drafts or committee drafts in any form for use by participants in the ISO standards development process is permitted without prior permission from ISO, neither this document nor any extract from it may be reproduced, stored or transmitted in any form for any other purpose without prior written permission from ISO.

Requests for permission to reproduce this document for the purpose of selling it should be addressed as shown below or to ISO's member body in the country of the requester:

[Indicate the full address, telephone number, fax number, telex number, and electronic mail address, as appropriate, of the Copyright Manger of the ISO member body responsible for the secretariat of the TC or SC within the framework of which the working document has been prepared.]

Reproduction for sales purposes may be subject to royalty payments or a licensing agreement.

Violators may be prosecuted.

Contents	Page

1	Scope	1

2	Document Structure	1

3	Symbols and Abbreviated Terms	1

4	MAR Domain and Concepts	3

4.1	Introduction	3

A MAR system requires real time processing [2]. For example, real time detection of faces with superimposed digital annotations is a MAR experience. The observation of superimposed annotations on a previously recorded video is not a MAR experience.	4

4.2	MAR Continuum	4

5	MAR Reference Model Usage Example	5

5.1	Designing a MAR Application or Service	5

5.2	Deriving a MAR Business Model	5

5.3	Extend Existing or Create New Standards for MAR	5

6	MAR Terminology	5

6.1	Mixed and Augmented Reality Experience	5

6.2	Mixed and Augmented Reality Engine	6

6.3	Mixed Reality System	6

6.4	Mixed and Augmented Reality System	6

6.5	Augmented Reality System	6

6.6	Augmented Virtuality System	6

6.7	Virtual Reality System	6

6.8	Physical Reality	6

6.9	Digital Object	6

6.10	Virtual World or Environment	7

6.11	MAR Scene Graph	7

Digital ObjectDigital Object	7

6.12	Virtualized Reality	7

6.13	Mixed Reality Continuum	7

6.14	Target object	7

6.15	Point(s) of Interest—POI	7

6.16	Augmentation	7

6.17	Sensor or Detector	7

6.18	Physical Sensor	7

6.19	Virtual Sensor	7

6.20	Real World/Object Capture Device	8

6.21	Recognizer	8

6.22	MAR Event	8

6.23	Tracker	8

6.24	Feature	8

6.25	Spatial Registration	8

6.26	Display	8

7	MAR Reference System Architecture	8

7.1	Overview	8

7.2	Viewpoints	9

7.3	Enterprise Viewpoint	10

7.3.1	Classes of Actors	10

7.3.2	Business Model of MAR Systems	12

7.3.3	Criteria for Successful MARS	12

7.3.4	Actor Requirements	13

7.4	Computation Viewpoint	13

7.4.1	Sensors: Pure Sensor and Real World Capturer	14

7.4.2	Recognizer and Tracker	15

7.4.3	Spatial Mapper	16

7.4.4	Event Mapper	16

7.4.5	Simulator	17

7.4.6	Renderer	17

7.4.7	Display / User Interface	18

7.4.8	MAR System API	19

7.5	Information Viewpoint	19

7.5.1	Sensors	19

7.5.2	Recognizer	20

7.5.3	Tracker	21

7.5.4	Spatial Mapper	21

7.5.5	Event Mapper	22

7.5.6	Simulator	22

7.5.7	Renderer	23

7.5.8	Display / User Interface	23

8	MAR Classification Framework	23

9	MAR System Types	25

9.1	MAR Type V—Visual Augmentation Systems	26

9.1.1	Local Recognition	26

9.1.2	Local Recognition and Tracking	26

9.1.3	Remote Recognition	27

9.1.4	Local Registration, Remote Recognition and Tracking	28

9.1.5	Local Tracking & Registration, Remote Recognition	28

9.1.6	Real Time, Remote Registration, Remote Detection, Local Presentation	29

9.2	MAR Type G: Points of Interest—GPS-based Systems	30

9.2.1	Content-embedded POIs	30

9.2.2	Server-available POIs	30

9.3	MAR Type 3DV: 3D Video Systems	31

9.3.1	Real Time, Local-Depth Estimation, Condition based Augmentation	31

9.3.2	Real Time, Local-depth Estimation, Model-based Augmentation	32

9.3.3	Real Time, Remote Depth Estimation, Condition-based Augmentation	33

9.3.4	Real Time, Remote-depth Estimation, Model-based Augmentation	33

9.4	MAR Type A: Audio Systems	34

9.4.1	Local Audio Recognition	34

9.4.2	Remote Audio Recognition	34

9.5	MAR Type 3A: 3D Audio Systems	36

9.5.1	Local Audio Spatialisation	36

10	Conformance	36

11	Performance	37

12	Safety	37

13	Security	38

14	Privacy	38

15	Use Case Examples and Coverage by the MAR Reference Model – Informative Clause	38

15.1	Introduction	38

15.2	Use Case Categories	38

15.2.1	Guide Use Case Category	38

15.2.2	Publish Use Case Category	39

15.2.3	Collaborate Use Case Category	39

15.3	MagicBook (Type V, Guide)	39

15.3.1	What it Does	39

15.3.2	How it Works	39

15.3.3	Mapping to MAR-RM and its Various Viewpoints	39

15.4	Human Pacman (Type G, Collaborate) and ARQuake (Type V and G, Collaborate)	40

15.4.1	What it Does	40

15.4.2	How it Works	40

15.4.3	Mapping to MAR-RM and Various Viewpoints	41

15.5	Augmented Haptics – Stiffness Modulation (Type H, Guide)	41

15.5.1	What it Does	41

15.5.2	How it Works	42

15.5.3	Mapping to MAR-RM and Various Viewpoints	42

15.6	Hear Through Augmented Audio (Type A, Guide)	42

15.6.1	What it Does	42

15.6.2	How it Works	43

15.6.3	Mapping to MAR-RM and Various Viewpoints	43

15.7	CityViewAR on Google Glass (Type G, Guide)	43

15.7.1	What it Does	43

15.7.2	How it Works	44

15.7.3	Mapping to MAR-RM and Various Viewpoints	44

15.8	Diorama—Projector-based Spatial Augmented Reality (Type 3DV, Publish)	44

15.8.1	What it does	44

15.8.2	How it Works	45

15.8.3	Mapping to MAR-RM and Various Viewpoints	45

15.9	Mobile AR with PTAM (Type 3DV, Guide)	46

15.9.1	What it Does	46

15.9.2	How it Works	46

15.9.3	Mapping to MAR-RM and Various Viewpoints	46

15.10	KinectFusion (Type 3DV, Guide)	47

15.10.1	What it Does	47

15.10.2	How it Works	47

15.10.3	Mapping to MAR-RM and Various Viewpoints	48

15.11	Use Case ARQuiz	48

15.11.1	What it Does	48

15.11.2	How it Works	49

15.11.3	Mapping to MAR-RM and Various Viewpoints	49

15.12	Use case Augmented Printed Material	49

15.12.1	What it Does	49

15.12.2	How it Works	50

15.12.3	Mapping to MAR-RM and Various Viewpoints	50

16	Extant AR-related solutions/technologies and their Application to the MAR Reference Model – Informative Clause	51

16.1	MPEG ARAF	51

16.2	KML/ARML/KARML	51

16.3	X3D	52

16.4	JPEG AR	52

16.5	Metaio SDK	53

16.6	ARToolKit/OSGART	54

16.7	Vuforia	54

16.8	Layar	54

16.9	Opens/OpenVX	54

Annex A  (informative)	55

Patent Statements	55

Foreword

ISO (the International Organization for Standardization) and IEC (the International Electrotechnical Commission) form the specialized system for worldwide standardization. National bodies that are members of ISO or IEC participate in the development of International Standards through technical committees established by the respective organization to deal with particular fields of technical activity. ISO and IEC technical committees collaborate in fields of mutual interest. Other international organizations, governmental and non-governmental, in liaison with ISO and IEC, also take part in the work. In the field of information technology, ISO and IEC have established a joint technical committee, ISO/IEC JTC 1.

International Standards are drafted in accordance with the rules given in the ISO/IEC Directives, Part 2.

The main task of the joint technical committee is to prepare International Standards. Draft International Standards adopted by the joint technical committee are circulated to national bodies for voting. Publication as an International Standard requires approval by at least 75 % of the national bodies casting a vote.

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. ISO and IEC shall not be held responsible for identifying any or all such patent rights.

ISO/IEC 18039 was prepared by Joint Technical Committee ISO/IEC JTC 1, Information technology, Subcommittee SC 24 and 29, Computer graphics, image processing and environmental data representation AND Coding of audio, picture, multimedia and hypermedia information.

This second/third/... edition cancels and replaces the first/second/... edition (), [clause(s) / subclause(s) / table(s) / figure(s) / annex(es)] of which [has / have] been technically revised.

Information technology — Computer graphics, image processing and environmental data representation and Coding of audio, picture, multimedia and hypermedia information — Mixed and Augmented Reality Reference Model

# Scope

The MAR (Mixed and Augmented Reality) Reference Model defines the scope of mixed and augmented reality, the main concepts, various terms and their definitions, and an overall system architecture. In particular, the MAR reference (architectural) model specifies a set of required submodules and their minimum functions, and associated information content and models that should be supported or provided by a MAR system. In addition, the reference model contains a list of representative system classes and use cases with respect to the proposed architecture model.

The reference model is intended to be used as a basic reference by any MAR-related Standards Development Organizations (SDOs) so that current and future international standards for MAR can be compared and their relationships be described. It can also be used as a guideline for MAR component, system, application and service developers as a means for fluid communication among MAR practitioners (see also Section 6). The reference model should apply to MAR systems independently of particular algorithms, implementation methods, computational platforms, display systems, and sensors and devices used.

This model does not define how specific MAR standards shall be defined and developed. In other words, it does not specify the functional descriptions of MAR, the bindings of those standards to programming languages, or the encoding of MAR information in any coding technique or interchange format. It is not intended to be an implementation specification for systems incorporating MAR.

MAR experiences are the result of creating, publishing and presenting content to users in context with the physical world. This reference model focuses on presenting MAR content. The creation and publishing of MAR experiences are out of scope of this standard.

# Document Structure

This document has the following structure. Section 3 introduces a set of symbols and abbreviated terms used within the document. Section 4 provides a definition of MAR and a description of various combinations of components in the real and virtual worlds. Section 5 explains how this standard should be used when designing a MAR application or service, when extending or designing new standards for MAR components and when designing a business model in the MAR market. Section 6 presents MAR terminology. Section 7 describes in detail the MAR reference system architecture and the associated viewpoints: enterprise, computational and informational. A MAR classification framework is presented in Section 8 and the MAR system classes in Section 9. Sections 10, 11, 12 and 13 highlight the importance of performance, safety, security and privacy when designing a MAR system. In Section 14, an extensive list of use case examples is presented, including a classification into three general classes. Finally, Section 15 presents extant AR-related solutions and technologies and their application to the MAR Reference Model.

# Symbols and Abbreviated Terms

| AR | Augmented Reality |
| --- | --- |
| ARAF | Augmented Reality Application Format |
| AVH | Aural/Visual/Haptics |
| AVR | Augmented Virtual Reality |
| CA | Content Aggregator |
| CC | Content Creator |
| DM | Device Manufacturer |
| DMCP | Device Middleware/Component Provider |
| EUP | End-user Profile |
| FoV | Field of View |
| GPS | Global Positioning System |
| MAR | Mixed and Augmented Reality |
| MARATC | MAR Authoring Tools Creator |
| MARE | Mixed and Augmented Reality Engine |
| MAREC | MAR Experience Creator |
| MAR-RM | Mixed and Augmented Reality Reference Model |
| MARS | Mixed and Augmented Reality System |
| MARSP | MAR Service Provider |
| MPEG | Motion Picture Experts Group |
| POI | Points of Interest |
| PTAM | Parallel Tracking and Mapping |
| SLAM | Simultaneous Localization and Mapping |
| SMCP | Service Middleware/Component Provider |
| TO | Telecommunication Operator |
| UI | User Interface |
| VR | Virtual Reality |
| X3D | eXtensible 3D |

# MAR Domain and Concepts

## Introduction

Mixed and Augmented Reality (MAR) refers to the human-observable result of combining components that represent on the one hand the real world and its objects, and on the other those that are virtual, synthetic and computer generated. The respective component can be represented and presented in many modalities (e.g., visual, aural, touch/haptics, olfactory, etc.) as illustrated in Figure 1. The figure shows a MAR system in which a virtual fish is augmented above a real world object (registered by using markers), visually, aurally and haptically.

Figure 1. The concept of MAR as combining representations of physical objects and computer mediated virtual ones in various modalities

Through such combinations, the physical (or virtual) object can be presented in an information-rich fashion through “augmentation” with the virtual (or real) counterpart. Thus, the idea of combining components is important for highlighting the mutual association between the physical and virtual worlds. This is also often referred to as “registration.”. The most typical registration is spatial, where the position and orientation of a real world object is computed and used to control the position and orientation of a Digital Object. The physical object may possess natural features that are easily recognizable or enriched with artifacts (e.g., markers). Temporal registration may also occur when the presence of a real object is detected and a Digital Object will be displayed. Registration may have various precision performances; it can vary in precision  (as illustrated in Figure 2). For example, in the spatial dimension, it can be measured in terms of distance or angles; in the temporal dimension in terms of milliseconds.

Figure 2. The notion of registration tightness: (left) virtual brain imagery tightly registered on a real human body image [1], (right) tourist information overlaid less tightly over a street scene [source Layar]

## A MAR system requires real time processing [2]. For example, real time detection of faces with superimposed digital annotations is a MAR experience. The observation of superimposed annotations on a previously recorded video is not a MAR experience.MAR Continuum

Since a MAR system or its contents combines real and virtual components, a MAR continuum can be defined according to the relative proportion of the real and virtual, encompassing the physical reality (“All Physical, No Virtual,” such as a live video) on one end, and the virtual reality (“All Virtual, No Physical,” such as a computer graphic object or scene) on the other end (illustrated in Figure 3. ). At any point on this continuum [3], i.e., a single instance of a system that uses a mixture of both reality and virtuality as a presentation medium is called a mixed reality system. In addition, for historical reasons, “mixed reality” is often synonymously or interchangeably used with augmented reality, which is actually a particular type of mixed reality (see Section 7). In this document we use the term mixed and augmented reality to avoid such confusion and emphasize that the same model applies to all combinations of real and digital components along the continuum. The two extreme ends in the continuum (the physical reality and the virtual reality) are not in the scope of this document.

Figure 3. The Mixed Reality (or Reality-Virtuality) Continuum

Two notable genres of MAR or points in the continuum are the Augmented Reality (AR) and Augmented Virtuality. An augmented reality system is a type of mixed reality system in which the medium representing the Digital Objects are embedded into the medium representing the physical world (e.g., video). In this case, the physical reality makes up a larger proportion of the final composition than the computer-generated information. An augmented virtuality system is a type of a mixed reality system in which the medium representing physical objects (e.g., video) are embedded into the computer-generated information (as illustrated in Figure 3).

# MAR Reference Model Usage Example

## Designing a MAR Application or Service

The MAR Reference Model is expected to be used as a reference guide in designing a MAR service and developing a MAR system, application, or content. With respect to the given application (or service) requirements, the designer may refer to, and select the needed components from those specified in the MAR model architecture. The functionalities, the interconnections between components, the data/information model for input and output, and relevant existing standards for various parts can be cross-checked to ensure generality and completeness. The classification scheme described in Section 9 can help the designer to specify a more precise scope and capabilities while the specific system classes defined in Section 10 can facilitate the process of model, system or service refinement.

## Deriving a MAR Business Model

The MAR reference model document introduces an enterprise viewpoint with the objective of specifying the industrial ecosystem, identifying the types of actors and describing various value chains. A set of business requirements is also expressed. Based on this viewpoint, companies may identify current business models or invent new ones.

## Extend Existing or Create New Standards for MAR

Another expected usage of the MAR Reference Model is in extending or creating new application standards for MAR functionalities. MAR is an interdisciplinary application domain involving many different technologies, solutions, and information models, and naturally there are ample opportunities for extending existing technology solutions and standards for MAR. The MAR Reference Model can be used to match and identify components for those that might require extension and/or new standardization. The computational and information models can provide the initial and minimum basis for such extensions or for new standards. In addition, strategic plans for future standardization can be made. In the case when competing de facto standards exist, the reference model can be used to make comparisons and evaluate their completeness and generality. Based on this analysis and the maturity of the standards, incorporation of de facto standards into open ones may be considered (e.g., markers, API, points of interest constructs, etc.).

# MAR Terminology

This section defines a set of MAR terms and sets a common vocabulary that MAR system developers, service operators and various actors can use.

## Mixed and Augmented Reality Experience

Mixed and Augmented Reality (MAR) Experience is the human-observed result of combining components that represent on the one hand the real world and its objects, and on the other those that are virtual, synthetic and computer generated.

The result of a system providing the user:

- A digital object displayed in the user’s field of view in response to detection of one or more triggers in the user’s proximity is a visual MAR experience.

- Digital audio as a result of detecting some trigger in the user’s proximity is an auditory MAR experience.

- A vibration, temperature change or introduction of another sign detectable by the user’s sense of touch as a result of detecting some trigger in the user’s proximity is a haptic MAR experience.

The trigger may be visual (computer vision), auditory (natural language), geospatial or detection of other environmental conditions such as radio signals. When the trigger is geospatial in nature, the experience is referred to as a Geospatial-based MAR Experience.

## Mixed and Augmented Reality Engine

Mixed and Augmented Reality Engine (MARE) is a collection of hardware and software elements that produce the result of combining components that represent on the one hand the real world and its objects, and on the other those that are virtual, synthetic and computer generated.

## Mixed Reality System

A system that uses mixture of physical world data and virtual world data representations as its presentation medium.

## Mixed and Augmented Reality System

A term that is synonymous with a mixed reality system. The word “augmented” is often used together with the word “mixed” for historical reasons.

## Augmented Reality System

A type of mixed reality system in which virtual-world data (e.g., computer-generated information) are embedded and registered in the physical-world data representation.

## Augmented Virtuality System

A type of mixed reality in which physical-world data (e.g., live video) are embedded and registered in the virtual-world data representation.

## Virtual Reality System

A system that uses only computer-generated information (i.e., Digital Objects).

## Physical Reality

A term synonymous with the physical world itself or a medium that represents the physical world (e.g., live video or raw image of the real world).

## Digital Object

A computer-generated entity. In the context of MAR, it usually has perceptual (e.g., visual, aural) characteristics and optionally, dynamic reactive behaviour.

## Virtual World or Environment

A spatial organization of multiple Digital Objects, potentially including global behaviour.

## MAR Scene Graph

A general data structure that arranges the logical and spatial representation of a graphical scene including the physical and digital worlds that is used by the MAR Engine to produce MAR experiences.

MAR Scene Graph content can be produced by MAR authoring tools and stored within or external to MAR-enabled applications.

## Digital ObjectDigital ObjectVirtualized Reality

A representation in a virtual environment of characteristics of the physical world.

## Mixed Reality Continuum

A spectrum spanning physical and virtual realities according to a proportional composition of physical and virtual data representations.

## Target object

A target physical object designed or chosen to allow easy detection, recognition and tracking (and finally augmentation). A target object represented by a 2D image is a target image.

## Point(s) of Interest—POI

A single target locations or collection of them. Aside from location data, POI is usually associated with metadata such as identifier and other location-specific information. Several POIs can be aggregated to define an area of interest.

## Augmentation

Digital Object data (computer-generated information) added on to, or associated with target physical object data in a MAR Scene Graph, or physical object data added on to, or associated with target Digital Object data.

## Sensor or Detector

A device that returns observed values related to a detected or measured condition or property. A sensor may be an aggregate of sensors.

## Physical Sensor

A sensor detecting or measuring a condition or property in the physical world.

## Virtual Sensor

A sensor detecting or measuring a condition or property in the virtual world.

## Real World/Object Capture Device

A sensor whose main purpose is the conversion of a physical reality representation to a real world or object data representation in a MAR system.

## Recognizer

A MAR component (hardware or software) that processes sensor output and generates MAR events based on conditions indicated by a content creator.

## MAR Event

A result of a detection of a condition relevant to MAR content (e.g., as a condition for augmentation).

## Tracker

A MAR component (hardware orsoftware) that analyses signals from sensors and provides some characteristics of a tracked entity (e.g., position, orientation, amplitude, or profile).

## Feature

Primitive geometric elements (e.g., points, lines, faces, colour, texture, shapes, etc.) or attributes of a given (usually physical) object used in its detection, recognition and tracking.

## Spatial Registration

The establishment of a spatial relationship or mapping between two models, typically between Digital Objectand target physical objects.

## Display

Device by which rendering results are presented to a user. It can use various modalities such as visual, auditory, haptics, olfactory, thermal, motion, etc. In addition, any actuator can be considered for display if it is controlled by a MAR system.

# MAR Reference System Architecture

## Overview

A Mixed and Augmented Reality (MAR) system requires several different components to fulfil its basic objectives: real time recognition of the physical world context, the registration of target physical objects with their corresponding Digital Objects, display of MAR content and handling of user interactions. A high-level representation of the typical components of a MAR system is illustrated in Figure 4. The central pink area indicates the scope of the MAR Reference Model. Blue round boxes are main computational modules and the dotted box represents the required information constructs.

Figure 4. Components of a MAR system

The MAR Simulation Engine has a key role in the overall architecture and is responsible for:

- Processing content as formalized in the MAR Scene Graph including additional media content provided in media assets.

- Processing user input.

- Processing the context provided by sensors capturing the real world.

- Managing the presentation of the final result (aural, visual, haptic and commands to additional actuators).

- Managing the communication with additional services.

## Viewpoints

In order to detail the global architecture presented in Figure 4, this reference model considers several analysis angles, called viewpoints, namely: Enterprise, Computation and Information. The definition of each viewpoint is provided in the following table.

Table 1. Definition of MAR viewpoints

| Viewpoint | Viewpoint Definition | Topics Covered by the MAR-Reference Model |
| --- | --- | --- |
| Enterprise | Articulates a business model that should be understandable by all stakeholders. This focuses on purpose, scope, and policies, and introduces the objectives of different actors involved in the field. | Actors and their roles Potential business models for each actor Desirable characteristics for the actors at both ends of the chain (creators and users) |
| Computational | Identifies the functionalities of system components and their interfaces. It specifies the services and protocols that each component exposes to the environment. | Services provided by each AR main component Interface description for some use cases |
| Information | Provides the semantics of information in the different components of the chain, the overall structure and abstract content type as well as information sources. It also describes how the information is processed inside each component. This viewpoint does not provide a full semantic and syntax of data but only a minimum of functional elements and should be used to guide the application developer or standard creator for creating their own information structures. | Context information such as spatial registration, captured video and audio, etc. Content information such as Digital Objects, application behaviour and user interaction management Service information such as remote processing of the context data |

## Enterprise Viewpoint

The Enterprise Viewpoint describes the actors involved in a Mixed and Augmented Reality System (MARS), their objectives, roles and requirements. The actors can be classified according to their role. There are four classes of actors.

### Classes of Actors

Figure 5. Enterprise Viewpoint of a MAR system: actors

Note: Acronyms used in the diagram above are described below, as well as in Section 3, “Symbols and abbreviated terms.”

Class 1: Providers of authoring or publishing capabilities

- MAR Authoring Tools Creator (MARATC)

  - A software platform provider of the tool used to create (author) a MAR-enabled Application or Service. The output of the MAR authoring tool is called a MAR Scene Graph.

- MAR Experience Creator (MAREC)

  - A person that designs and implements a MAR-enabled Application or Service.

- Content Creator (CC)

  - A designer (person or organization) that creates multimedia content (scenes, objects, etc.).

Class 2: Providers of MAR Engine components (MARE)

- Device Manufacturer (DM)

  - An organization that produces devices in charge of augmentation and used as end-user terminals.

  - An organization that produces devices in charge of augmentation and used as end-user terminals.

- Device Middleware/Component Provider (DMCP)

  - An organization that creates and provides hardware, software and/or middleware for the augmentation device. In this category belong modules such as:

    - Multimedia player or browser engine provider (rendering, interaction engine, execution, etc. ).

    - Context knowledge provider (satellites, etc.).

    - Sensor manufacturers (inertial, geomagnetic, camera, microphone, etc.).

Class 3: Service Providers

- MAR Service Provider (MARSP)

  - An organization that offers discovery and/or delivery services.

- Content Aggregator (CA)

  - An organization aggregating, storing, processing and serving content.

- Telecommunication Operator (TO)

  - An organization that manages telecommunication among other actors.

- Service Middleware/Component Provider (SMCP)

  - An organization that creates and provides hardware, software and/or middleware for processing servers. This category includes services such as:

    - Location providers (network-based location services, image databases, RFID based location, etc.).

  - Semantic provider (indexed image or text databases, etc.).

Class 4: MAR User

- MAR Consumer/End-User Profile (EUP)

  - A person who experiences the real world synchronized with digital assets. He/she uses a MAR Scene Graph, a MAR Engine and MAR Services in order to satisfy information access and communication needs. By means of their digital information display and interaction devices, such as smart phones, desktops and tablets, users of MAR hear, see and/or feel digital information associated with natural features of the real world, in real time.

Several types of actors from the list above can commercially exploit a MAR system.

### Business Model of MAR Systems

The actors in the MAR system have different business models:

- A MAR Authoring Tools Creator may provide the authoring software or content environment to a MAR Experience Creator. Such a tool ranges in complexity from full programming environments to relatively easy-to-use online content creation systems.

- The Content Creator (CC) prepares a digital asset (text/picture/video/3D model/animation) that may be used in the MAR experience.

- A MAR Experience Creator (MAREC) creates a MAR experience in the form of a MAR Rich Media Representation. He/she can associate media assets with features in the real world, thereby transforming them into MAR-enabled digital assets. The MAREC also defines the global/local behaviour of the MAR experience. The creator should consider the performances of obtaining and processing the context as well as performance of the AR Engine. A typical case would be one where the MAREC will specify a set of minimal requirements that should be satisfied by the hardware or software components.

- A middleware/component provider produces the components necessary for core enablers to provide key software and hardware technologies in the fields of sensors, local image processing, display, remote computer vision and remote processing of sensor data for MAR experiences. There are two types of middleware/component providers: device (executed locally) and services (executed remotely).

- MAR Service Provider is a broad term signifying an organization that supports the delivery of MAR experiences. This can be via catalogues or to assist in discovering a MAR experience.

### Criteria for Successful MARS

The requirements for the successful implementation of MARS are expressed with respect to two types of actors. While the end user experience for MAR should be more engaging than browsing Web pages, it should be possible to create, transport and consume MAR experiences with the same ease as is currently possible for web pages.

### Actor Requirements

MAR Experience Creator requirements:

- Tools for authoring workflows for both non-technical people and experts.

- Authoring and seamless integration of indoor and outdoor MAR experiences.

- Authoring of MAR experiences independently of user location and registration technology.

- Augmentation of information for (at least) the aural and/or visual senses and, in general, for all the human senses, in a realistic manner.

- Incorporation of MAR experiences in existing applications and services.

- Connection availability to additional data providers, service providers, etc., not originally intended to be used in MAR experiences.

MAR End-User requirements:

- Accurate real time registration of the MAR experience with the real world, and composition in a natural-synthetic scene, based on context (e.g., geospatial coordinates, vision, etc.).

- Automatic, continuous consideration of user context in consuming the MAR experience (e.g., user profile, user interaction, user preference, user location, device status, etc.).

## Computation Viewpoint

The Computation Viewpoint describes the overall interworking of a MAR system. It identifies major processing components (hardware and software), defines their roles and describes how they interconnect.

Figure 6. Computation Viewpoint of a MAR system

### Sensors: Pure Sensor and Real World Capturer

A Sensor is a hardware (and optionally) software component able to measure any kind of physical property. In the context of MAR, a sensor is mainly used to detect, recognize and track the target physical object to be augmented. In this case, it is a “pure sensor.” Another use of a sensor is to capture and stream to the Simulator, the data representation of the physical world or objects for producing a MAR Experience. In this case, it is called a “real world capturer.” A typical example is the video camera that captures the real world as a video to be used as a background in an augmented reality experience. Another example is “Augmented Virtuality,” where a person is filmed in the real world and the corresponding video is embedded in a virtual world. Note that the captured real world data can be in any modality such as visual, aural, haptic, etc.

A sensor can measure different physical properties, and interpret and convert these observations into digital signals. The captured data can be used (1) to only compute the context in the tracker/recognizer, or (2) to both compute the context and contribute to the composition of the scene. Depending on the nature of the physical property, different types of devices can be used (cameras, environmental sensors, etc.). One or more sensors can simultaneously capture signals.

The input and output of the Sensors are:

- Input: Real world signals.

- Output: Sensor observations with or without additional metadata (position, time, …).

The Sensors can be categorized as follows:

Table 2. Sensor categories

| Dimension | Types |
| --- | --- |
| 1. Modality/type of the sensed/captured data | Visual | Auditory | Electro-magnetic waves (e.g., GPS) | Haptic/tactile | Temperature | Other physical properties |
| 2. Liveness of sensed/captured data | Live | Pre-captured | — | — | — | — |

### Recognizer and Tracker

The Recognizer is a hardware or software component that analyses signals from the real world and produces MAR events and data by comparing with a local or remote target signal (i.e., target for augmentation).

The Tracker is able to detect and measure changes of the properties of the target signals (e.g., pose, orientation, volume, etc.).

Recognition can only be based on prior captured target signals. Both the Recognizer and Tracker can be configured with a set of target signals provided by, or stored in an outside resource (e.g. third-party database server) in a consistent manner with the MAR Scene Graph.

Recognizer and Tracker can be independently implemented and used.

- The input and output of the Recognizer are:

  - Input: Raw or processed signals representing the physical world (provided by sensors) and target object specification data (reference target to be recognized).

  - Output: At least one event acknowledging the recognition.

Table 3. Recognizer categories

| Dimension | Types |
| --- | --- |
| 1. Form of target signal | 2D image patch | 3D primitives (lines, faces, points) | 3D model | Location (e.g., earth- reference coordinates) | Audio patch | Other |
| 2. Form of the output event | Indication only of recognized event | Additional data such as data type, timestamp, recognition confidence level, other attributes | — | — | — | — |
| 3. Place of execution | Local | Remote (server, cloud, etc.) | — | — | — | — |

- The input and output of the Tracker are:

  - Input: Raw or processed signals representing the physical world and target object specification data (reference target to be recognized).

  - Output: Instantaneous values of the characteristics (pose, orientation, volume, etc.) of the recognized target signals.

Table 4. Tracker categories

| Dimension | Types |
| --- | --- |
| 1. Form of target signal | 2D image patch | 3D primitives (lines, faces, points) | 3D Model | Location (e.g., earth- reference coordinates) | Other |
| 2. Form of the output event | Spatial (2D, 3D, 6D, …) | Aural (intensity, pitch, …) | Haptic (force, direction, …) | Others | — |
| 3. Place of execution | Local | Remote (server, cloud, etc.) | — | — | — |

### Spatial Mapper

The coordinate systems and spatial metrics used in a given sensor need to be mapped into that of the MAR Scene Graph so that the sensed real object can be correctly placed, oriented and sized. The role of the Spatial Mapper is to provide spatial relationship information (i.e., position, orientation, scale and unit) between the physical space and the space of the MAR Scene Graph by applying the necessary transformations for the calibration. The spatial relationship between a particular sensor system and a target augmented space is provided by the MAR Experience Creator and is maintained by the Spatial Mapper.

- The input and output of the Spatial Mapper are:

  - Input: Sensor identifier and sensed spatial information.

  - Output: Calibrated spatial information for the given MAR Scene Graph.

The notion of the Spatial Mapper can be extended to mapping other domains such as audio (e.g., direction, amplitude, units, scale) and haptics (e.g., direction, magnitudes, units and scale).

### Event Mapper

The Event Mapper creates an association between a MAR Event obtained from the Recognizer or the Tracker and the condition specified by the MAR Content Creator in the MAR Scene Graph.

It is possible that the descriptions of the MAR events produced by the Recognizer or the Tracker are not the same as those used by the Content Creators even though they are semantically equivalent. For example, a recognition of a particular location (e.g., longitude of -118,24 and latitude of 34.05) might be identified as  “MAR_location_event_1,” while the Content Creator might refer to it in a different vocabulary or syntax, e.g., as “Los Angeles, CA, USA.”

The event relationship between a particular recognition system and a Target Object is provided by the MAR Experience Creator and is maintained by the Event Mapper.

- The input and output of the Event Mapper are:

  - Input: Event identifier and event information.

  - Output: Translated event identifier for the given MAR Scene Graph.

### Simulator

The Simulator constitutes the core of any MAR system. Its main purpose is to interpret the sensed data to further recognize and track the target data to be augmented, import the real world or object data, simulate the augmented world, compose the real and virtual data representation together for proper rendering in the required modalities (e.g. visually, aurally, haptically). The Simulator might require additional and external media assets or computational services for supporting these core functionalities.  The Simulator can be part of a MAR Engine able to load a full scene graph description (including assets, scene behaviour, user interaction, …) for its simulation and presentation or part of a stand-alone application with pre-programmed behaviour.

The Simulator is a software component capable of (1) loading the MAR Scene Graphdescription as provided by the MAR Experience Creator or processing the MAR Scene Graphas specified by the application developer, (2) interpret data provided by various mappers, user interactions, sensors, local and/or remote services, (3) execute and simulate scene behaviours, (4) compose various types of media representations (aural, visual, haptics, etc.).

- The input and output of the Simulator are:

  - Input: MAR Scene Graphdescription, user input, (mapped) MAR events and external service events.

  - Output: an updated version of the scene description.

The Simulator might be categorized according to the following dimensions:

Table 5. Simulator categories

| Dimension | Types |
| --- | --- |
| 1. Space & time | 2D + time | 3D + time | — | — |
| 2. User interactivity | Yes | No | — | — |
| 3. Execution place | Local | Remote | Hybrid | — |
| 4. Number of simultaneous users | Single-user | Multi-user | — | — |

### Renderer

The Renderer refers to the software and optional hardware components for producing, from the MAR Scene Graph description (updated after a tick of simulation), a presentation output in a proper form of signal for the given display device. Note that the rendered output (and the associated displays) can be in any modality. When multiple modalities exist, they need to be synchronized in proper dimensions (e.g., temporally and/or spatially).

- The input and output of the Renderer are:

  - Input: (Updated) MAR Scene Graph data.

  - Output: Synchronized rendering output (e.g., visual frame, stereo sound signal, motor commands, etc.).

The Renderer can be categorized in the following way:

Table 6. Renderer categories

| Dimension | Types |
| --- | --- |
| 1. Modality | Visual | Aural | Haptics | Others |
| 2. Execution place | Local | Remote | Hybrid | — |

### Display / User Interface

The Display is a hardware component that produces the actual presentation of the MAR Scene Graphto the end-user in different modalities. Examples include monitors, head-mounted displays, projectors, scent diffusers, haptic devices and sound speakers. A special type of display is an actuator that does not directly stimulate the end-user senses but may produce a physical effect in order to change some properties of the physical objects or the environment.

- The input and output of the Display are:

  - Input: Render signals

  - Output: Display output

- The input and output of the UI are:

  - Input: User action

  - Output: UI event

The Displays may be categorized according to their modalities with each of them having their own attributes as follows:

Table 7. Visual display categories

| Dimension | Types |
| --- | --- |
| 1. Presentation | Optical see through | Video see through | Projection | — |
| 2. Mobility | Fixed | Mobile | Controlled | — |
| 3. No. of channels | 2D (mono) | 3D stereoscopic | 3D holographic | — |

Table 8. Aural display categories

| Dimension | Types |
| --- | --- |
| 1. No. of channels | Mono | Stereo | Spatial | — |
| 2. Acoustic space coverage | Headphones | Speaker | — | — |

Table 9. Haptics display categories

| Dimension | Types |
| --- | --- |
| Type | Vibration | Pressure | Temperature | Other |

The UI is a hardware component used to capture user interaction (touch, click) for the purpose of modifying the state of the MAR Scene Graph. The UI requires sensors to achieve this purpose. However, these sensors may have a similar usage as those known as pure sensors. The difference consists then in the fact that the only physical object sensed is the user.

Table 10. UI categories

| Dimension | Types |
| --- | --- |
| Type | Click | Drag and drop | Touch | Natural interface (voice, facial expression, gestures, etc.) |

### MAR System API

The MAR components defined in the Computation Viewpoint may have an exposed Application Programming Interface, thereby simplifying application development and integration. Additionally, higher-level APIs can be specified in order to make abstractions for often-used MAR functionalities and data models in the following way (not exhaustive):

- Defining the markers and target objects for augmentation.

- Setting up multi-markers and their relationships.

- Setting up and representing the virtual/physical camera and viewing parameters.

- Detection and recognition of markers/target objects.

- Managing markers/target objects.

- Extracting specific spatial properties and making geometric/matrix/vector computations.

- Loading and interpreting MAR Scene Graph.

- Calibrating sensors and virtual/augmented spaces.

- Mapping of MAR events between those that are user defined and those that are system defined.

- Making composite renderings for specific displays, possibly in different modalities.

Such APIs are designed to simplify the development of special-purpose MAR systems.

## Information Viewpoint

The Information Viewpoint provides some key semantics of information associated with the different components of the chain, including the semantics of input and output for each component as well as the overall structure and abstract content type. This viewpoint does not provide a full semantic and syntax of data but only a minimum of functional elements and it should be used to guide the application developer or standard creator in creating their own information structures. Let us note that for some components, there are already standards available providing full data models.

### Sensors

This component is a physical device characterized by a set of capabilities and parameters. A subclass of Sensors is the Real World Capturer whose output is an audio, video or haptics stream to be embedded in the MAR Scene Graphor analysed by specific hardware or software components. Additionally, several parameters are associated with the device or with the media captured such as intrinsic parameters (e.g., focal length, field of view, gain, frequency range, etc.), extrinsic parameters (e.g., position and orientation), resolution, sampling rate. The captured audio data can be mono, stereo or spatial. The video can be 2D, 3D (colour and depth) or multi-view. As an example, the following table illustrates possible sensor specifications:

Table 11. Sensor attribute example

| Sensor Attribute | Values |
| --- | --- |
| Identifier | “Sensor 1”, “Sensor 2”, “My Sensor”, etc. |
| Type | Video, audio, temperature, depth, image, etc. |
| Sensor specific attributes | 120° (field of view), 25 (frequency), 41000 (sampling rate), etc. |

The input and output of the Sensors are:

- Input: Real world (no information model is required).

- Output: Sensor observations (optionally post-processed in order to extract additional metadata such as position, time, etc.). They depend on the type of the sensor used (e.g., binary image, colour image, depth map, sound stream, force, etc.).

### Recognizer

There are two types of information used by the recognizer: the sensor’s output and the target physical object representation. By analysing this information, the Recognizer will output a MAR event.

- The input data model of the Recognizer is the output of the sensors.

- The target physical object data should contain the following elements. First, it will have an identifier indicating the event when the presence of the target object is recognized. The target physical object specification may include raw template files used for the recognition and matching process such as image files, 3D model files, sound files, etc. In addition to the raw template files or data, it could also include a set of feature profiles. The types of features depend on the algorithms used by the Recognizer. For instance it could be a set of visual feature descriptors, 3D geometric features, etc..

Table 12. Target physical object attribute

| Target Physical Object Attribute | Values |
| --- | --- |
| Recognition event identifier | “Image_1”, “Face_Smith”, “Location_1”, “Teapot3d”, etc. |
| Raw template file / data | hiro.bmp, smith.jpg, teapot.3ds, etc. |
| Feature set definition | Set of visual features, set of aural features, set of 3D geometry features, etc. |

- The output is an event that at least identifies the recognized target, and optionally provides additional information, that should follow a standard protocol, language, and naming convention. As an example, the following table illustrates possible event specification.

Table 13. Attributes for the Recognizer output

| Attribute | Values |
| --- | --- |
| Identifier | “Event 1”, “Location 1”, “My_Event”, etc. |
| Type | Location, Object, Marker, Face, etc. |
| Value | Paris, Apple, HIRO, John_Smith, etc. |
| Time stamp | 12:32:23, 02:23:01 |

### Tracker

There are two types of information used by the Recognizer: the sensors output and the target physical object representation. By analysing this information, the Tracker will output a MAR event.

- The input data model of the Recognizer is the output of the sensors.

- The target physical object data should contain the same elements as for Recognizer.

- Output : A continuous stream of instantaneous values of the characteristics (pose, orientation, volume, etc.) of the recognized target signals.

Table 14. Attribute for the Tracker output

| Attribute | Values |
| --- | --- |
| Identifier (of the stream of tracking data) | “GPS_location_stream”, “Marker_location_stream”, “Object_orientation_stream”, etc. |
| Type | Location, object, marker, face, etc. |
| Tracking data (elements of the stream) | Inertial position, 4x4 transformation matrix, current volume level, current force level, etc. |
| Optional: Time stamp | 12:32:23, 02:23:01 |

### Spatial Mapper

In order to map the physical sensor space into the MAR Scene Graph, explicit mapping information must be supplied by the content or system developer. The spatial mapping information can be modelled as a table with each entry characterizing the translation process from one aspect of the spatial property (e.g., lateral unit, axis direction, scale, etc.) of the sensor to the given MAR Scene Graph. There is a unique table defined for a set of sensors and a MAR Scene Graph.

Table 15. Spatial mapping table example

| Sensor 1 | MAR Scene Graph1 |
| --- | --- |
| ID_235 (Sensor ID) | MyMarkerObject_1 (a scene graph node) |
| Sensor position and orientation | T (3.0, 2.1, 5.5), R (36°, 26°, 89°). Used to convert from physical space to the scene space (align the coordinate systems) |
| Scale in (X, Y, Z) | (0.1, 0.1, 0.1). Used to convert from physical space to the scene space (align the coordinate systems) |

### Event Mapper

In order to map MAR Events as defined by the content developer or specified within the MAR Scene Graph, as well as events identified and recognized by the Recognizer, a correspondence table is needed. The table provides the matching information between a particular recognizer identifier and an identifier in the MAR Scene Graph. There is a unique table defined for a set of events and a MAR Scene Graph.

| Event Set | MAR Scene GraphEvent Set |
| --- | --- |
| Location =(2.35, 48.85) | Location= Paris, France |
| R_event_1 | My_Event_123 |
| Right_Hand_Gesture | OK_gesture |

### Simulator

The Simulator has several inputs. The main input is the MAR Scene Graphthat contains all information about how the MAR Experience Creator set up the MAR experience, such as:

- Initial scene description including spatial organisation.

- Scene behaviour.

- Specification of the representation of the real objects to be detected and tracked (targeted for augmentation) as well as the virtual assets to be used for augmentation, and the association between the representation of the real objects and their corresponding synthetic assets.

- The calibration information between the sensor coordinate system and the MAR scene coordinate system (supplied to the Spatial Mapper).

- The mapping between identifiers or conditions outputted by the recognizer or tracker and elements of the MAR Scene Graph (supplied to the Event Mapper).

- The set of sensors and actuators used in the MAR experience.

- The way in which the user may interact with the physical world or digital objects.

- Access to remote services like maps, image databases, processing servers, etc..

The Simulator output is an “updated” scene graph data structure.

### Renderer

The input of the AHV Renderer is an updated scene graph.

The output is a visual, aural or/and haptic stream of data to be fed into display devices (such as a video frame, stereo sound signal, motor command, pulse-width modulation signal for vibrators, etc.).

The MAR system can specify various capabilities of the AHV Renderer, so the scene can be adapted and simulation performance can be optimized. For instance, a stereoscopic HMD and a mobile device might require different rendering performances. Multimodal output rendering might necessitate careful millisecond-level temporal synchronization.

| Render Type | Capability Dimensions |
| --- | --- |
| Visual | Screen size, resolution, field of vew (FoV), number of channels, signal type |
| Aural | Sampling rate, number of channels, maximum volume |
| Haptic | Resolution, operating spatial range, degrees of freedom, force range |

### Display / User Interface

The input of the Display is a stream of visual, aural and/or haptics data.

The output of the UI is a set of signals to be sent to the Simulator in order to update the scene.

# MAR Classification Framework

This section introduces a classification framework serving to translate abstract MAR Reference Model concepts into real world MAR implementations. Several examples will illustrate how to apply the Computation and Information viewpoints to develop specific MAR types.

Table 16. MAR classification framework

| Component | Dimension | Types |
| --- | --- | --- |
| Pure Sensors | Modality | Visual | Auditory | Electro-magnetic waves (e.g., GPS) | Haptic/tactile | Temperature | Other physical properties |
|  | Source type | Live | Pre-captured | — | — | — | — |
| Real World Capturer | Modality | Visual | Auditory | Haptics properties | Other | — | — |
|  | Form of visual modality | Still image | 2D video | 3D video (video + depth) | 3D mesh | Other | — |
|  | Source type | Live | Pre-captured | — | — | — | — |
| Recognizer | Form of target signal | Image patch | 3D primitives | 3D model | Location (e.g., earth- reference coordinates) | Audio patch | Other |
|  | Form of the output event | Recognized or not | Additional data: Type, timestamp, recognition confidence level, other attributes | — | — | — | — |
|  | Execution pace | Local | Remote | — | — | — |  |
| Tracker | Form of target signal | Image patch | 3D primitives | 3D Model | Earth- reference coordinates | Audio patch | Other |
|  | Form of the output event | Spatial (2D, 3D, 6D, etc.) | Aural (intensity, pitch, …) | Haptic (force, direction, …) | — | — | — |
|  | Execution place | Local | Remote | — | — | — | — |
| Space Mapper | Space type | Spatial | Audio | Haptics | Others | — | — |
| Event Mapper | Modality | Visual | Temporal | Aural | Location | Others | — |
| Simulator | Space & time | 2D + t | 3D + t | — | — | — | — |
|  | User interactivity | Yes | No | — | — | — | — |
|  | Execution place | Local | Remote | Hybrid | — | — | — |
|  | Number of simultaneous users | Single-user | Multi-user | — | — | — | — |
| Renderer | Modality | Visual | Aural | Haptics | Other | — | — |
|  | Execution place | Local | Remote | Hybrid | — | — | — |
| Visual Display | Presentation | Optical see through | Video see through | Projection | — | — | — |
|  | Mobility | Fixed | Mobile | Controlled | — | — | — |
|  | No of channels | 2D (mono) | 3D stereoscopic | 3D holographic | — | — | — |
| Aural Display | No of channels | Mono | Spatial | — | — | — | — |
|  | Acoustic space coverage | Headphones | Speaker | — | — | — | — |
| Haptics Display | Type | Vibration | Pressure | Temperature | — | — | — |
| UI | Interaction type | Touch | Click | Drag | Gesture | Other | — |

# MAR System Types

This section uses the classification framework provided in the previous section to describe several types of mixed and augmented reality application or services. Each type focuses on parts of the system architecture and provides illustrations of how to use the reference model. The types are defined as illustrated in Table 17. An instance of a MAR system can be a combination of several types.

Table 17. MAR types

| MAR TypeType V | The type of MAR systems augmenting the 2D visual data captured by a real camera |
| --- | --- |
| MAR Type R | The type of MAR systems augmenting the 2D visual data continuously captured by one or several real cameras and reconstructing the 3D environment (note: SLAM, PTAM) |
| MAR Type A | The type of MAR systems augmenting the aural modality |
| MAR Type H | The type of MAR systems augmenting the haptics modality |
| MAR Type G | The type of MAR systems using global position system to register synthetic objects in the real world |
| MAR Type 3DV | The type of MAR systems augmenting the 3D visual data captured by multiple cameras or video plus depth cameras |
| MAR Type 3DA | The type of MAR systems augmenting the scene by using 3D audio data |

Note: Other MAR system types may be added in the future.

## MAR Type V—Visual Augmentation Systems

### Local Recognition

The Device detects the presence of target images (or the corresponding descriptors) in a video stream. The video can be the result of real time scene capture using a local camera, a remote video source or a pre-recorded video stored in the device. The content specified in the Information Viewpoint is:

    - The set of target images (raw or corresponding descriptor).

    - URL of the video stream (camera, remote video source or local track).

Figure 7. Local recognition

### Local Recognition and Tracking

The Device detects the presence of target images (or corresponding descriptors) in a video stream, computes the transformation matrix (position, orientation and scaling) of the ones detected and augments the video stream with associated graphical objects. The video can be the result of a real time scene capture using a local camera, a remote video source or a video track stored in the device. The content specified in the Information Viewpoint is:

- The set of target images (raw or corresponding descriptor).

- URL of the video stream (a local camera, a local video track or a remote video resource).

- Media used for the augmentation.

Figure 8. Local recognition and tracking (Pose Matrix or PM)

### Remote Recognition

The Device sends the target images (or the corresponding descriptors) and the video stream sampled at a specified frame rate (provided by a local camera, a local video track or a remote video resource) to a Processing Server which detects the target resources in the video stream. An ID mask of the detected resources is returned. The content specified in the Information Viewpoint is:

- Target images (or the corresponding descriptors).

- URL of the video stream (a local camera, a local video track or a remote video resource).

- URL of the Processing Servers.

Figure 9. Remote recognition

In addition, a communication protocol has to be implemented between the MAR Engine and the Processing Servers.

### Local Registration, Remote Recognition and Tracking

The Device sends the target images (or the corresponding descriptors) and the video stream sampled at a specified framerate (provided by a local camera or a local video track or a remote video resource) to a Processing Server which detects and tracks the target resources in the video stream. An ID mask and the computed transformation matrix of the detected resources are returned. The content specified in the Information Viewpoint is:

- Target images (or the corresponding descriptors).

- URL of the video stream (a local camera, a local video track or a remote video resource).

- Media used for the augmentation.

- URL of the Processing Servers.

Figure 10. Local registration, remote recognition and tracking

In addition, a communication protocol has to be implemented between the MAR Engine and the Processing Servers.

### Local Tracking & Registration, Remote Recognition

The Device sends video samples (from local camera capture, a local video track or remote video resources) to a Processing Server that is analysing the frames and detects one or several target images stored in its local database. The server returns the position and size of one or several target images detected in the frame, as well as the augmentation content (Digital Objects, application behaviour). By using position and size, the device will crop the target images from the frame and use them for local tracking. The content specified in the Information Viewpoint is:

- URLs of the Processing Servers.

- URL of the video stream (a local camera, a local video track or a remote video resource).

Figure 11. Local tracking & registration, remote recognition

In addition, a communication protocol has to be implemented between the MAR Engine and the Processing Servers.

### Real Time, Remote Registration, Remote Detection, Local Presentation

The Device sends the target images (or the corresponding descriptors) and the video stream sampled at a specified framerate (provided by a local camera, a local video track or a remote video resource) to a Processing Server which detects and tracks the target resources in the video stream. Additionally, the Processing Server does the augmented composition and rendering, and sends back to the device the composed video stream. The content specified in the Information Viewpoint is:

- Target images (raw or descriptor).

- URL of the video stream (a local camera, a local video track or a remote video resource).

- URL of the Processing Servers.

Figure 12. Remote registration, remote recognition and local presentation

In addition, a communication protocol has to be implemented between the MAR Engine and the Processing Server.

## MAR Type G: Points of Interest—GPS-based Systems

### Content-embedded POIs

An MAR EngineMAR Engine is used by the end-user to open an AR file containing (locally in the scene) POIs from a specific region. The POIs are filtered with respect to user preferences as follows: Either the engine has access to a local resource (file) containing predefined POI-related user preferences or the engine exposes an interface allowing users to choose (on the fly) their preferences. The POIs corresponding to the user selections/preferences are displayed. The AR content also describes how the POIs are displayed, either on the map or in AR view, by creating MapMarker instances and using the metadata provided by the POIs. The content specified in the Information Viewpoint is:

  - POI data.

  - The MapMarker shape (representation).

  - Referenced by the ARAF Browser.

  - User preferences (optional).

Figure 13. Content-embedded POI

### Server-available POIs

An MAR Engine is used by the end-user to open an AR file. One or multiple URLs to POI providers are specified in the AR content. The POIs are filtered with respect to user preferences as follows: Either the engine has access to a local resource (file) containing predefined POI-related user preferences or the engine exposes an interface allowing users to choose (on the fly) their preferences. The POIs corresponding to user selections/preferences are requested from the specified URLs and displayed. The AR content describes how POIs are displayed, either on the map or in AR view, by creating MapMarker instances and using the metadata provided by the POIs. The content specified in the Information Viewpoint is:

  - URLs of the POI providers.

  - The MapMarker shape/representation.

In addition, a communication protocol should be established between the MAR Engine and the POI Provider.

Figure 14. Server available POI

## MAR Type 3DV: 3D Video Systems

### Real Time, Local-Depth Estimation, Condition based Augmentation

Example: The end-user has an augmented reality experience where one digital object is displayed on a horizontal plane detected within a ray of 10m.

The Device captures multi-view video and estimates depth. This representation is used to detect conditions imposed by the content designer. Once the condition is met, the Device renders the Digital Object by using the scale and orientation specified by the content designer. The content specified in the Information Viewpoint is:

    - Media used for the augmentation.

    - The orientation and scale of the Digital Object (uniform/isotropic  scaling representing physical units).

    - The condition (e.g., horizontal plane within a ray of 10m).

Figure 15. Real-time, local depth estimation, condition based augmentation

### Real Time, Local-depth Estimation, Model-based Augmentation

A content designer captures offline an approximation of the real world as a 3D model and then authors content by adding additional 3D Digital Objects registered within an approximation of the real world. The end-user navigates in the real world using a multi-view camera. The Device estimates the depth and computes the transformation matrix of the camera in the real world by matching the captured video and depth data with the 3D model approximating the real world. The augmented scene is therefore rendered by using the transformation matrix result. The content specified in the Information Viewpoint is:

    - Digital objects and their local transformations in the MAR Experience.

    - The approximation of the 3D model of the real world.

Figure 16. Real-time, local depth estimation, model-based augmentation

### Real Time, Remote Depth Estimation, Condition-based Augmentation

Example: The end-user has an augmented reality experience where one digital object is displayed on a horizontal plane detected within a radius of 10m.

The Device captures multi-view video, sends synchronized samples to a Processing Server that estimates the depth. This representation is sent to the device and the server uses it to detect conditions imposed by the content designer. The server sends as well the transformation matrix that the Device uses to render the Digital Object by using the scale specified by the content designer. The content specified in the Information Viewpoint is:

    - Media used for the augmentation.

    - The orientation and scale of the Digital Object (uniform/isotropic  scaling representing physical units).

    - The condition (e.g. horizontal plane within a ray of 10m).

    - URL of the Processing Server.

Figure 17. Real Time, remote-depth estimation, condition-based augmentation

### Real Time, Remote-depth Estimation, Model-based Augmentation

A content designer captures offline an approximation of the real world as a 3D model and then authors content by adding additional 3D Digital Objects registered within the approximation of the real world. The end-user navigates in the real world using a multi-view camera. The captured video stream is sent to the Processing Server, which computes the depth as well as the transformation matrix of the camera in the real world. Information is sent back to the Device that uses them for augmentation. The content specified in the Information Viewpoint is:

  - Digital objects and their local transformations in the MAR Experience.

  - An approximation (3D model) of the real world.

  - URL of the Processing Server.

Figure 18. Real Time, remote-depth estimation, model-based augmentation

## MAR Type A: Audio Systems

### Local Audio Recognition

The Device detects the presence of a sound (or the corresponding descriptors) in an audio stream. Audio can result from a real time capture using a local microphone, a remote audio source or a pre-recorded audio stored in the device. The content specified in the Information Viewpoint is:

    - The set of target audio samples (raw or corresponding descriptor).

    - The URL of the audio stream (microphone, remote audio source or local track).

Figure 19. Local audio recognition

### Remote Audio Recognition

The Device sends target audio samples (or corresponding descriptors), as well as the audio stream sampled at a specified framerate (provided by a local microphone, a local audio track or a remote audio resource) to a Processing Server, which detects the target resources in the audio stream. An ID mask of the detected resources is returned. The content specified in the Information Viewpoint is:

- Target audio samples (or the corresponding descriptors).

- URL of the audio stream (local microphone, a local audio track or a remote audio resource).

- URL of the Processing Server.

Figure 20. Remote audio recognition

In addition, a communication protocol has to be implemented between the MAR Engine and the Processing Server.

A variation of this scenario is one in which the MAR Engine extracts compact descriptors from the captured audio data and sends them to the Processing Server, as illustrated in the figure below.

Figure 21. Remote audio recognition with descriptors transmission

## MAR Type 3A: 3D Audio Systems

### Local Audio Spatialisation

The Device computes the spatial audio data (left and right channels) by using the original audio data and the relative position between the user and the audio Digital Object used for augmentation.

The content specified in the Information Viewpoint is:

    - Target audio samples (raw or corresponding descriptors).

    - URL of the audio stream (microphone, remote audio source or local track).

Figure 22. Local audio recognition

# Conformance

Conformance to this reference model is expressed by describing how the aspects of a MAR implementation relates to the MAR system architecture.  Conformance of MAR implementations to this standard shall satisfy at least the following requirements.

- The following key architectural components, as specified in the Reference Model, shall be present in a given MAR implementation: Display / UI, Event Mapper, Recognizer, Renderer, Sensors, Simulator, Spatial Mapper Tracker and a mapping between a MAR implementation components and the Reference Model components can be established and evaluated.

- The relationship between the implementation of these architectural components shall conform to those in this Reference Model, as specified in 7.4 and graphically depicted in Figure 6.

- The interfaces between the architectural components of a MAR implementation shall contain and carry the information specified in 7.4 and 7.5.  However, the specific content, format, data types, handshake, flow, and other implementation details is at the discretion of the given MAR implementation to meet its specific needs.

- The API for a MAR implementation shall conform to the concepts specified in 7.4.8 and 7.5 in order to ensure compatibility and software interface interoperbility between MAR implementations, which can be accomplished at least at the abstract API level.

# Performance

The system performance guideline defines the minimum operational level of MAR systems and establishes possible conformance issues.  There are several metrics that can be used to benchmark a MAR system, defined at various component levels or at the global level. For the latter case, augmentation precision and speed in different operating conditions are the most relevant. Specifying performance metrics is outside the scope of the MAR Reference Model, however, several examples are provided for use by other benchmarking systems:

- Augmentation precision can be measured by the error between the virtual camera parameters, estimated by the tracker and the correct ones or by the distance (in pixels) and angular distance (in degrees)  between the place where the Digital Object is displayed and the one where it should be displayed.

- The latency can be measured as the total time needed to process the target object and produce the augmentation.

- The operating conditions may include lighting conditions, mobility of the target object, sensing distance and orientation, etc.

# Safety

MAR systems are used by human users to interact in the real world and they entail various safety issues.  For example, most MAR systems require the use of special displays and artificial augmentations which may steer users’ attention away and create potentially dangerous situations.  Minimum safety guidelines are necessary to ensure that the given MAR system and contents includes components for safeguarding the user during the usage of the system.  Note that the issue of performance is closely related to that of safety. Development of policies or software that increases the safety of users, assets and systems, will reduce risks resulting from:

- Obstruction of dangerous conditions that could lead to injury of humans during MAR system use.

- Hardware necessary for MAR system operation that has not been safety certified for specific environments.

- Lack of sufficient instructions, presentations, and highlighting of information for safe and proper usage of the MAR contents,

- Non-ergonomic design causing visual, aural and haptic interferences.

- Distraction of attention.

- Temporary disconnection of the network service causing false confidence in the currently presented information.

- Not considering special operational safety and health (OSH) requirements (e.g. such as in construction zones, traffic, operating vehicles, working at heights in proximity to hazards, etc.).

- Human movements necessary for operating a MAR system.

- Insufficient level of performance for requirements of MAR system-assisted tasks.

- Accessibility issues for users with impairments deserve special consideration.

- Sickness from mismatched stimuli to the human vestibular system. restricted field of view, and other potential factors.  Disruptive effects may in turn lead to disorientation, nausea, blurred vision, loss of spatial acuity, and multiple other symptoms.  These symptoms may last even after the use of MAR systems and services.

# Security

Most MAR system services and implementations, like many other modern information systems, often rely on network based solutions and are prone to the usual information security problems.  Even as a stand-alone system, many MAR applications and services, by nature, tend to deal with large amounts of personal information, therefore posing as an attractive target for security attacks.  The MAR reference model outlines the minimum set of features and components for architects and developers to consider for the sake of general security:

- Encrypt digital assets.

- Encrypt sensor readings captured by MAR systems.

- Encrypt other communications between MAR components.

# Privacy

Personal privacy and potential exposure of personal information to unauthorized systems or third parties via cameras or other sensors on the MAR-assisted device is out of scope of the MAR Reference Model but is highly relevant to the adoption of MAR systems. Developers may consider how to use existing or new systems and include components in their MAR systems that:

- Authenticate user identity (e.g., registration with an account).

- Authorize system access to users’ personal data.

- Define the duration of periods during which data access and/or storage is authorized.

# Use Case Examples and Coverage by the MAR Reference Model – Informative Clause

## Introduction

This section introduces use case categories and examples for MAR, and for each example provides the mapping to the MAR system architecture and corresponding viewpoints.

## Use Case Categories

### Guide Use Case Category

The simplest and most fundamental use case category is Guide. In the Guide type of experience, a user points sensors at a target physical object (or in a direction) and queries the system. The system provides a user interface for Digital Objects about which a person asks one or more questions, often in a sequence. Experiences in the Guide use case category often leads user in learning, completing a task or arriving at a destination (navigation).

### Publish Use Case Category

The Publish use case category permits a user to “author” a new Digital Object in the form of text, image, video or audio and to attach this user-generated information to a real physical object target. The user expresses an opinion, provides additional thoughts or asks questions, and other people with permissions to access the Digital Object will be able to see, hear or feel it.

### Collaborate Use Case Category

The Collaborate Use Case category encompasses all use cases in which there is the physical world, digital assets and two or more users interacting with one another in real time. In Collaborate, there is no prior limit to where users are in the physical world with respect to one another.

A specific Collaborate use case can specify the distance between users (proximity) in meters. Other use cases can specify categories of objects that constitute the focus of attention. For example, there are use cases in this category involving manufacturing, repair, maintenance of machinery, infrastructure or some stationary, man-made object. Other use cases in this category are multi-player AR-assisted games.

## MagicBook (Type V, Guide)

### What it Does

MagicBook [4] is a marker-based augmented reality system. Animated 3D models and other types of Digital Objects are added to the printed book content. It helps convey information that is difficult to express solely with print. In addition, it allows a transition into a pure VR mode.

Figure 23. A user viewing the MagicBook using a hand-held video see through display

### How it Works

A marker is printed in a book and viewed using a video see-through display as illustrated in the figure above. The marker is recognized and tracked by the camera attached to the display.

### Mapping to MAR-RM and its Various Viewpoints

| MAR-RM Component | Major Components in the MagicBook |
| --- | --- |
| Sensor | Camera |
| Real world capture | Live video |
| Target physical object | 2D marker |
| Tracker / Recognizer | Template-based recognition/homography-based 2D marker tracking |
| Spatial mapping | Hard coded |
| Event mapping | Hard coded |
| Simulator | Hard coded |
| Rendering | OpenGL |
| Display / UI | Video see-through and headphone |

## Human Pacman (Type G, Collaborate) and ARQuake (Type V and G, Collaborate)

### What it Does

Human Pacman [5] is an outdoor interactive entertainment system in which the video game Pacman (developed by Namco in 1980) is played outdoors with humans acting as pacmen and ghosts. Virtual cookies are overlaid in the physical environment. ARQuake [6] is an outdoor interactive entertainment system developed in 2000 using markers.

Figure 24. The view of Human Pacman as seen by the user (left). AR Quake: a first-person outdoor AR game using a marker instead (right)

### How it Works

The user wears a head-mounted display whose location is tracked by a GPS system. In Pacman, virtual cookies appear properly registered in the real world and are also mapped by their GPS coordinates. Users interact with the virtual cookies and other users (e.g., ghosts) and have a similar behaviour as in the conventional “Pac-Man” game.

### Mapping to MAR-RM and Various Viewpoints

| MAR-RM Component | Major Components in Human Pacman | Major Components in AR Quake |
| --- | --- | --- |
| Sensor | Camera/GPS | Camera/GPS/compass |
| Real-world capture | Live video | Live video |
| Target physical object | Location | Location/direction/marker |
| Tracking/recognition | GPS | Camera/GPS/compass |
| Spatial mapping | Hard-coded earth referenced | Hard coded |
| Event mapping | Hard coded | Hard coded |
| Simulation Engine | Hard coded | Hard coded |
| Rendering | Generic graphic subsystem | Quake game ported |
| Display/UI | Video see-through, head phone, hand-held keyboard and mouse and other touch sensors | Video see-through, head phone, button device |

## Augmented Haptics – Stiffness Modulation (Type H, Guide)

### What it Does

In this use case, a user feels the response force of an object as well as the augmented response force of a Digital Object. It can be used for instance in training for cancer palpation on a dummy mannequin [7].

Figure 25. The stiffness modulation system

### How it Works

A manipulator-type haptic device is used to sense and capture the force from a real object. Both the haptic probe and user’s hand are mechanically tracked. A collision with a Digital Object is simulated and its added reaction force is computationally created and displayed through the haptic probe.

### Mapping to MAR-RM and Various Viewpoints

| MAR Reference Model Component | Major Components in the Augmented Haptics |
| --- | --- |
| Sensor | Force and joint sensors on the haptic manipulator |
| Real-world capture | Force sensor |
| Target object | Any 3D physical object |
| Tracker | Joint sensor on the haptic manipulator and kinematic computation |
| Recognizer | No recognition |
| Spatial mapping | Hard coded |
| Event mapping | Hard coded |
| Simulation Engine | Hard coded |
| Rendering | In-house force rendering algorithm |
| Display / UI | Haptic manipulator |

## Hear Through Augmented Audio (Type A, Guide)

### What it Does

Composition of real world sound and computed generated audio [8].

Figure 26. Hear-through augmented audio using a bone-conducting headset

### How it Works

A bone-conduction headset is used to add augmented sound to real-world sound. It is considered a “hear through” because the augmented media is merged and perceived by the human rather than as a result of a computed composition.

### Mapping to MAR-RM and Various Viewpoints

| MAR-RM Component | Major Components in the Augmented Audio |
| --- | --- |
| Sensor | None |
| Real-world capture | Direct capture by human ear |
| Target object | Real-world sound |
| Tracking/Recognition | Hard coded |
| Spatial mapping | Hard coded |
| Event mapping | None |
| Simulation Engine | None |
| Rendering | HRTF-based rendering of 3D sound |
| Display | Bone-conduction headset |

## CityViewAR on Google Glass (Type G, Guide)

### What it Does

CityViewAR [9] is a mobile outdoor AR application providing geographical information visualization on a city scale. It was developed in Christchurch, New Zealand, which was hit by several major earthquakes in 2010 and 2011. The application provides information about destroyed buildings and historical sites that were affected by the earthquakes.

Figure 27. CityViewAR as seen through optical see-through Google glass

### How it Works

Geo-located content is provided in a number of formats including 2D map views, AR visualization of 3D models of buildings on-site, immersive panorama photographs, and list views. GPS-based tracking is implemented on Android-based smartphone platforms and is displayed through an optical see-through Google Glass.

### Mapping to MAR-RM and Various Viewpoints

| MAR-RM Component | Major Components in the CityViewAR |
| --- | --- |
| Sensor | GPS and compass |
| Real-world capture | None |
| Target physical object | Location |
| Tracker/recognizer | GPS and compass |
| Spatial mapping | Absolute earth reference |
| Event mapping | Hard coded for location and direction |
| Simulation Engine | Hard coded |
| Rendering | Text and image |
| Display | Optical see through |

## Diorama—Projector-based Spatial Augmented Reality (Type 3DV, Publish)

### What it does

The Diorama [10] is a spatially augmented reality system for augmenting movable 3D objects in an indoor environment by using multiple projectors. The augmentation is made directly on the target physical object.

Figure 28. The user interacts with a house-shaped object, which is augmented with a different painting

### How it Works

A projector illuminates augmentation on an object that is tracked by an optical tracker. A user applies a paintbrush that is also tracked. The paintbrush is used to create an image that is projected on the physical object after a calibration process. The geometry of the target physical object is known in advance.

### Mapping to MAR-RM and Various Viewpoints

| MAR-RM Component | Major Components in the Diorama |
| --- | --- |
| Sensor | Optical tracker |
| Real-world capture | None |
| Target object | A preconfigured 3D physical object |
| Tracking/Recognition | Optical tracker |
| Spatial mapping | Hard coded |
| Event mapping | Hard coded/user input |
| Simulation Engine | None |
| Rendering | Image |
| Display | Projector |

## Mobile AR with PTAM (Type 3DV, Guide)

### What it Does

PTAM [11] is a mobile AR application that augments the environment, based on tracking and mapping natural features such as 3D points.

Figure 29. PTAM tracking and mapping of 3D point features and augmenting on a virtual plane

### How it Works

A simplified single camera based the SLAM [12] algorithm is used. The tracking and mapping tasks are split in order to operate in parallel threads. One thread deals with the task of robust tracking of the mobile device, while the other constructs a probabilistic 3D point map from a series of video frames through cycles of prediction and correction.

### Mapping to MAR-RM and Various Viewpoints

| MAR-RM Component | Major Components in the PTAM |
| --- | --- |
| Sensor | Camera |
| Real-world capture | Live video |
| Target object | Particular 3D points in the environment |
| Tracker/Recognizer | Image-processing software |
| Spatial mapping | Relative to a calibration object |
| Event mapping | None |
| Simulation Engine | Hard coded |
| Rendering | OpenGL ES |
| Display | Mobile phone screen |

## KinectFusion (Type 3DV, Guide)

### What it Does

KinectFusion [13] is a system for accurate real time mapping of complex and arbitrary indoor scenes and objects, using a moving depth camera. Using reconstructed 3D information about the environment, a more effective augmentation is possible for solving the occlusion problem and enabling physical simulations (e.g., rendering augmentation behind real objects).

Figure 30. Capturing the depth image of a scene, performing its 3D reconstruction (above) and carrying out physical simulation with thousands of virtual balls

### How it Works

The depth data streamed from a movable Kinect depth sensor are fused into a single global surface model of the observed scene in real time. At the same time, the current sensor pose is obtained by tracking the live depth frame relative to the global model using a coarse-to-fine iterative closest-point algorithm.

### Mapping to MAR-RM and Various Viewpoints

| MAR-RM Component | Major Components in the KinectFusion |
| --- | --- |
| Sensor | Kinect (depth sensor and video camera) |
| Real-world capture | Live 3D video |
| Target object | 3D physical object |
| Tracking/Recognition | Depth image processing software |
| Spatial mapping | None |
| Event mapping | None |
| Simulation Engine | Hard coded |
| Rendering | Generic graphics engine |
| Display | Any |

## Use Case ARQuiz

### What it Does

ARQuiz [14] is an augmented reality location-based game for smartphones and tablets, based on the MPEG ARAF standard. The game consists of answering questions related to physical places that are being visited by players. Each question has an associated hint. A hint is a short story that eventually helps the player to find the correct answer to a given question. All hints are placed on a specific route that the user has to follow in order to advance in the game. The hints are visible on a map (MAP view). As every hint is represented by the same icon on the map, the player does not know which hint corresponds to his current question. This is the reason why the player has to use the AR view where the hints are represented by numbered 3D spheres. Once the correct number has been identified (it is visible in the AR view), the player has to “catch” that sphere by getting closer to it (five meters or less). When close enough to the hint, the corresponding story is displayed on the device’s screen. By reading the story, the player eventually finds the correct answer of the question but may also discover more details about the place he or she is visiting at that specific moment.

Figure 31. Views from AR Quiz game

### How it Works

A smartphone on which an ARAF Browser is installed needs to be used to open and run the game file. A GPS signal and an Internet connection are needed in order to play the game. The game is an MP4 file that encapsulates the textual data (ARAF-compliant file), as well as additional media that is linked in the game file. The ARAF-compliant file consists of BIFS content in which the interface and the logic of the game are described. Being an AR location-based game, the ARAF Browser needs to access GPS data, as well as the orientation sensors of the device in order to place the Digital Objects at the correct positions in the augmented reality (camera) view.

### Mapping to MAR-RM and Various Viewpoints

| MAR-RM Component | Major Components in the ARQuiz |
| --- | --- |
| Sensor | GPS and orientation |
| Real-world capture | Live video |
| Target physical object | Location |
| Tracker/recognizer | GPS and orientation |
| Spatial mapping | Absolute earth reference |
| Event mapping | Hard coded for location |
| Simulation Engine | Hard coded |
| Rendering | Text, images and 3D graphics |
| Display | Mobile phone screen |

## Use case Augmented Printed Material

### What it Does

Augmented Printed Material [15] is an AR application that enriches (physical) printed material with any digital media-like videos, images, sounds or 3D graphics. The application presents the user additional information related to the printed material that he or she is reading. An Augmented Printed Material application can enrich anything from a simple book to a tourism guide, a city map or a newspaper.

Figure 32. Examples of augmenting printed content

### How it Works

The application uses ARAF-compliant content that can be read by any ARAF Browser. The user opens the application and starts pointing the camera to the pages of the printed material that he or she is reading. Digital representations (e.g., screenshots) of the printed material pages to be augmented and their corresponding augmentation media are used as input to the application. As long as the application’s scanning mode is active, camera frames are processed and matched against target images submitted by the Content Creator. Once an image has been recognized, a tracking algorithm is then used to compute the relative position (pose matrix) of the recognized target image in the real world. The application is programmed to overlay the associated augmentation media on top of the recognized physical material as long as the physical printed material is being tracked.

### Mapping to MAR-RM and Various Viewpoints

| MAR-RM Component | Major Components in the Augmented Printed Material |
| --- | --- |
| Sensor | Live sensed camera data |
| Real world capture | Live video |
| Target physical object | Printed material |
| Tracker/recognizer | Image processing software (image recognition and tracking) |
| Spatial mapping | Relative to a recognized object |
| Event mapping | Hard coded |
| Simulation Engine | Hard coded |
| Rendering | Text, images and 3d graphics |
| Display | Mobile phone screen |

# Extant AR-related solutions/technologies and their Application to the MAR Reference Model – Informative Clause

## MPEG ARAF

The Augmented Reality Application Format (ARAF) is an ISO standard published by MPEG and can be used to formalize a full MAR experience. It consists of an extension of a subset of the MPEG-4 Part 11 (Scene Description and Application Engine) standard, combined with other relevant MPEG standards (MPEG-4 Part 1, MPEG-4 Part 16, MPEG-V) and is designed to enable the consumption of 2D/3D multimedia, interactive, natural and virtual content. About two hundred nodes are standardized in MPEG-4 Part 11, allowing various kinds of scenes to be constructed. ARAF refers to a subset of these nodes. The data captured from sensors or used to command actuators in ARAF are based on ISO/IEC 23005-5 data formats for interaction devices (MPEG-V Part 5). MPEG-V provides an architecture and specifies associated information representations to enable the representation of the context and to ensure interoperability between virtual worlds. Concerning mixed and augmented reality, MPEG-V specifies the interaction between the virtual and real worlds by implementing support for accessing different input/output devices, e.g., sensors, actuators, vision and rendering and robotics. The following sensors are used in ARAF: Orientation, position, acceleration, angular velocity, GPS, altitude, geomagnetic and camera.

The ARAF concept is illustrated in the figure below. It allows the distinction between content creation (using dedicated authoring tools) and content “consumption” (using platform-specific AR engines). Authors can specify the MAR experience by only editing the ARAF content.

Figure 33. The ARAF concept

By using ARAF, content creators can design MAR experiences covering all types defined in Section 9, from location-based services to image-based augmentation, from local to cloud-assisted processing. ARAF also supports natural user interaction, 3D graphics, 3D video and 3D audio media representation, as well as a variety of sensors and actuators.

## KML/ARML/KARML

KML (Keyhole Mark-up Language) [16] offers simple XML-based constructs for representing a physical GPS (2D) location and associating text descriptions or 3D model files to it. KML has no further sensor-related information, and thus the event of location detection (whichever way it is found by the application) is automatically tied to the corresponding content specification. KML is structurally difficult to be extended for vision-based AR (which requires a 3D scene graph-like structure) and more sophisticated augmentation can be added only in an ad hoc way.

ARML (AR Mark-up Language) [17] is an extension to KML and allows for richer types of augmentation for location-based AR services. KARML [18] goes a bit further by adding even more decorative presentation styles (e.g., balloons, panoramic images, etc.), but more importantly, it proposes a method of relative spatial specification of the augmented information for their exact registration. These KML-based approaches use OGC standards for representing GPS landmarks, but for the rest, they use a mixture of non-standard constructs, albeit being somewhat extensible (perhaps in an ad hoc way and driven mostly by specific vendor needs), for augmentation (e.g., vs. HTML or X3D).

Figure 34. Content models of KML, ARML and KARML

## X3D

X3D [19] is a royalty-free ISO standard XML-based file format for representing 3D computer graphics. It is a successor to the Virtual Reality Modelling Language (VRML).  X3D features extensions to VRML (e.g., CAD, Geospatial, Humanoid animation, NURBS, etc.), the ability to encode the scene graph using an XML syntax as well as the Open Inventor-like syntax of VRML97, or binary formatting, and enhanced application programming interfaces (APIs). In essence, it can be used to represent a 3D virtual scene with dynamic behaviours and user interaction.

In 2009 an X3D AR working group has been set up to extend its capability for MAR functionalities. These include additional constructs and nodes for representing live video, physical and virtual camera properties, ghost objects, MAR events and MAR visualization.

## JPEG AR

# The JPEG AR describes a mechanism of JPEG image-based AR at an abstraction level, without specifying the syntaxes and protocols. Currently, there are three interest points in JPEG AR frameworks: interface, application description and JPEG file format.

# For the interface, there are four main perspectives that are taken into account:

- Interface between the Sensor and AR Recognizer/AR Tracker

- For this interface, we specify information that needs to be transmitted from the Sensor to the Recognizer/Tracker.

- Interface between the AR Recognizer/AR Tracker and the Event Handler

- For this interface, we specify data and information that needs to be composed in the Recognizer/Tracker and transmitted to the Event Handler. This transmitted data and information is necessary for the Event Handler to process described operations according to the information.

- Interface between the Event Handler and the Content Repository

- For this interface, we specify information and corresponding operations that the Event Handler and Content Repository manipulate.

- Interface between the Event Handler and Renderer

- For this interface, we specify information that is transmitted from the Event Handler to the Renderer for displaying composite images.

Figure 35. JPEG AR framework architecture

## Metaio SDK

The Metaio SDK is an augmented reality Software Development Kit (SDK) for creating AR applications on Android, iOS, PC and Mac. Development can be done using the SDK's native APIs or cross-platform using AREL. AREL (Augmented Reality Experience Language) uses a custom XML format and describes the entire AR experience and contains:

- The content of an AR experience, such as location based POIs, 3D models and/or images.

- The relation of content in respect to reference coordinate systems.

- Proprietary XML-based configuration files of Metaio's tracking system, which defines coordinate systems and sensors to use.

- Application logic that defines the behaviour and interaction within the AR experience.

The application logic uses the AREL JavaScript API, which provides a mapping from JavaScript to the Metaio SDK API. This allows the developer to implement complex AR functionalities.

The Metaio SDK provides several tracking strategies such as 2D and 3D markerless tracking, SLAM, fiducial marker tracking and GPS/compass/accelerometer-based tracking.

## ARToolKit/OSGART

ARToolKit [20] is a computer tracking library for the purpose of creating augmented reality applications that overlay Digital Objects in the real world. It uses video tracking capabilities that calculate the real camera position and orientation relative to square physical markers in real time. Once the real camera position is known, a virtual camera can be positioned at the same point and 3D computer graphics models can be precisely overlaid on the real marker. ARToolKit provides solutions for two of the key problems in augmented reality: viewpoint tracking and Digital Object interaction. ARToolkit, which by itself does not have any scene graph support, has been merged with an open source virtual reality platform (with scene graph support), namely the OpenSceneGraph (OSG) [21].  This version of OSG is called the OSGART.

## Vuforia

Vuforia [22] is an augmented reality Software Development Kit (SDK) for mobile devices that enables the creation of Reality applications. It uses Computer Vision technology to recognize and track planar images (image targets) and simple 3D objects, such as boxes, in real time. This image registration capability enables developers to position and orient Digital Objects, such as 3D models and other media, in relation to real world images when these are viewed through the camera of a mobile device. The Digital Object then tracks the position and orientation of the image in real time so that the viewer’s perspective on the object corresponds with their perspective on the image target, so that it appears that the Digital Object is a part of the real world scene. The computationally intensive recognition functions are carried out in a remote server with the local client program managing the communication and target object capture, which makes it ideal for MAR application development on mobile devices.

## Layar

Layar [23] has a simple internal content model consisting of a direct association of a POI to augmentation (services) provided by networked servers (using a JSON protocol). However, the exact model structure is hidden from the user. To create a “layer” (like a content snippet), the user simply uses a web-based tool to create a POI and specify details of the web server supplying the augmentation service, which is stored in a central server to be processed by the Layar browser.

## Opens/OpenVX

OpenCV (Open Source Computer Vision) [24] is a library of programming functions mainly aimed at real time computer vision, developed by the Intel Russia research center in Nizhny Novgorod, and now supported by Willow Garage and Itseez. It is free for use under the open source BSD license. The library is cross-platform. It focuses mainly on real time image processing. If the library finds Intel's Integrated Performance Primitives on the system, it will use these proprietary optimized routines to accelerate itself.  As a basic library for computer vision, it is often used as a means for implementing many MAR systems and content.

The Khronos group has developed a similar standard for such a computer vision library called OpenVX, which lends itself to hardware acceleration and higher performance.

- (informative)

Patent Statements

The International Organization for Standardization and the International Electrotechnical Commission (IEC) draw attention to the fact that it is claimed that compliance with this part of ISO/IEC 14496 may involve the use of patents.

ISO and IEC take no position concerning the evidence, validity and scope of these patent rights.

The holders of these patent rights have assured the ISO and IEC that they are willing to negotiate licences under reasonable and non-discriminatory terms and conditions with applicants throughout the world. In this respect, the statements of the holders of these patent rights are registered with ISO and IEC. Information may be obtained from the companies listed below.

Attention is drawn to the possibility that some of the elements of this part of ISO/IEC 18039 may be the subject of patent rights other than those identified in this annex. ISO and IEC shall not be held responsible for identifying any or all such patent rights.

| Company | Address |
| --- | --- |
| none |  |

# Bibliography

Ferenc A Jolesz, Image-guided procedures and the operating room of the future, Harvard Medical School, Boston, MA, http://www.spl.harvard.edu/archive/spl-pre2007/pages/papers/horizon/horizon.html.

Azuma, Ronald T. A Survey of Augmented Reality. Presence: Teleoperators and Virtual Environments 6, 4 (August 1997), pp. 355 - 385. Earlier version appeared in Course Notes #9: Developing Advanced Virtual Reality Applications, ACM SIGGRAPH 1995 (Los Angeles, 6-11 August 1995), 20-1 to 20-38.

Milgram, Paul; H. Takemura, A. Utsumi, F. Kishino (1994). "Augmented Reality: A class of displays on the reality-virtuality continuum". Proceedings of Telemanipulator and Telepresence Technologies. pp. 2351–34.

Mark Billinghurst, Hirokazu Kato, Ivan Poupyrev, The MagicBook: A transitional AR interface, Computers & Graphics, Volume 25, Issue 5, October 2001, Pages 745-753.

Adrian David Cheok, Kok Hwee Goh, Wei Liu, Farzam Farbiz, Siew Wan Fong, Sze Lee Teo, Yu Li, Xubo Yang, Human Pacman: a mobile, wide-area entertainment system based on physical, social, and ubiquitous computing, Personal and Ubiquitous Computing, (2004) 8: 71–81, 2004.

Bruce Thomas, Ben Close, John Donoghue, John Squires, Phillip De Bondi, Michael Morris, Wayne Piekarski, ARQuake: An outdoor/indoor augmented reality first person application, Proc. of ISWC, 2000.

Seokhee Jeon and Seungmoon Choi, Real Stiffness Augmentation for Haptic Augmented Reality, Presence: Teleoperators and Virtual Environments, vol. 20, no. 4, pp. 337-370, 2011.

Robert Lindeman, Haruo Noma, Paul de Barros, An empirical study of hear-through augmented reality: using bone conduction to deliver spatialized audio, , Proc. of IEEE VR, 2008.

Gun Lee, Andreas Dunser, Senugwon Kim and Mark Billinghurst, CityViewAR: a mobile outdoor AR application for city visualization, Proc. of ISMAR, 2012.

Deepak Bandyopadhyay, Ramesh Raskar, Henry Fuchs, Dynamic Shader Lamps: Painting on Movable Objects, Proc. of ISAR, 2001.

George Klein and David Murray, Parallel tracking and mapping for small AR workspaces, Proc. of ISMAR, 2007.

A. Davison, I. Reid, N. D. Molton, and O. Stasse, MonoSLAM: Realtime, single camera SLAM. IEEE Trans. Pattern Analysis and Machine Intelligence, 2007.

Richard Newcombe, Shahram Izadi, Otmar Hillinges, David Molyneaux, and David Kim, KinectFusion: Real time dense surface mapping and tracking, Proc. of ISMAR 2011.

http://youtu.be/la-Oez0aaHE.

https://www.youtube.com/watch?v=CNcgxEOt_rM.

OGC, KML/OGC, www.opengeospatial.org/standards/kml.

Mobilizy, ARML Specification for Wikitude 4, http://www.openarml.org/wikitude4.html.

Hill, MacIntyre, Gandy, Davidson and Rouzati, Khamra-KML/HTML Augmented Reality Mobile Architecture, https://research.cc.gatech.edu/polaris.

Web3D, What is X3D?, http://www.web3d.org/about/overview.

http://en.wikipedia.org/wiki/ARToolKit-

www.openscenegraph.org-

http://en.wikipedia.org/wiki/Vuforia_Augmented_Reality_SDK-

Layar, http://www.layar.com-

http://en.wikipedia.org/wiki/OpenCV-

# Footnotes

Illustration provided by Magic Vision Lab, University of South Australia.

Some of the use cases are commercial solutions and may have related intellectual property rights.

http://dev.metaio.com/sdk/

http://dev.metaio.com/arel/overview/

http://dev.metaio.com/sdk/documentation/tracking-config/

# Comments

It would be helpful to have these in alphabetical order.

Browser or engine?

Watch line spacing. Here it was multiple 1.15 but in other places single.

Subclass or subtype?

Other tables use lower case for dimensions

I would capitalize words as much as possible

Replace “MAR Engine” in all figures “MAR Engine”

Browser or engine?

At the end of all this, it would be good to have a last review (as you suggested), with an eye especially to final formatting, such as appropriate page breaks and repeat table header for tables that break across pages.

The conventional game is actually referred to as Pac-Man

Needs a page break during final formatting

Since you’re using bold in many tables, make sure table headings are bolded everywhere

Browser or engine?

Browser or engine?

Formatting? This section is at the bottom of the page.